## Slide 1: The HYMOD model
 |  | meaning | min | max
1 | SM | maximum soil moisture (mm) | 0 | 400
2 | beta | exponent in the soil moisture routine (-) | 0 | 2
3 | alfa | partition coefficient (-) | 0 | 1
4 | Rs | slow reservoir coefficient (1/Dt) | 0 | 0.1
5 | Rf | fast reservoir coefficient (1/Dt) | 0.1 | 1
FAST FLOW ROUTING
SLOW FLOW ROUTING
streamflow
rainfall R
SOIL MOISTURE ACCOUNTING
SF2
SF3
SF1
RFSFi
aRE
SS
RSSS
discharge RE = (1 - (1-S/SM)b ) R
S
Q
evaporation
EA = (S/SM)) EP
Boyle, D. (2001). Multicriteria calibration of hydrological models. PhD thesis, Dep. of Hydrol. and Water Resour., Univ. of Ariz., Tucson.
Wagener, T., D. Boyle, M. J. Lees, H. S. Wheater, H. V. Gupta, and S. Sorooshian (2001), A framework for development and application of hydrological models, Hydrol. Earth Syst. Sci., 5(1), 13-26.
This is part of SAFE Toolbox: bristol.ac.uk/cabot/resources/safe-toolbox/ by F. Pianosi, F. Sarrazin and T. Wagener

## Slide 2: The HBV model
# | NAME | MEANING | UNITS | MIN | MAX
1 | BETA | Exponential parameter in soil routine | (-) | 0 | 7
2 | LP | Limit for potential evapotranspiration | (-) | 0.3 | 1
3 | FC | Maximum soil moisture content | (mm) | 1 | 2000
4 | PERC | Maximum flow from upper to lower tank | (mm/Dt) | 0 | 100
5 | K0 | Near surface flow coefficient |  | 0.05 | 2
6 | K1 | Recession coefficient for upper tank | (1/Dt) | 0.01 | 1
7 | K2 | Recession coefficient for lower tank | (1/Dt) | 0.05 | 0.10
8 | UZL | Near surface flow threshold | (mm) | 0 | 100
9 | MAXBAS | Transfer function parameter | (day) | 1 | 6
CFLUX
LZ
UZ
R
PERC
EA
FC
SM
P
LP
Q1
Q0
MAXBAS
Parameters:
Seibert, J. (1997), Estimation of Parameter Uncertainty in the HBV Model, Nordic Hydrology, 28(4/5), 247-262.
This is part of SAFE Toolbox: bristol.ac.uk/cabot/resources/safe-toolbox/ by F. Pianosi, F. Sarrazin and T. Wagener
Kollat, J.B., Reed, P.M, Wagener, T. (2012) When are multiobjective calibration trade-offs in hydrologic models meaningful? Water Resources Research, 48, W03520
R = P x (SM/FC)BETA
Q0 =K1xUZ + K0x(UZ-UZL) Q1=K2 x LZ
Notes: Why systematic

## Slide 3: The snow accumulation/melting routine
Precipitation
Temperature
Separation between rainfall and snowfall
Dynamics of snowpack (solid and liquid component)
Flow exiting from the snowpack
Ts
CFMAX
CFR
CWH
Kollat, J.B., Reed, P.M, Wagener, T. (2012) When are multiobjective calibration trade-offs in hydrologic models meaningful? Water Resources Research, 48, W03520
 | meaning | min | max
Ts | threshold temperature [C] | -3 | 3
CFMAX | degree day factor [mm/C] | 0 | 20
CFR | refreezing factor [-] | 0 | 1
CWH | Water holding capacity of snow [-] | 0 | 0.8
Parameters:
This is part of SAFE Toolbox: bristol.ac.uk/cabot/resources/safe-toolbox/ by F. Pianosi, F. Sarrazin and T. Wagener